## Slide 1: Multi-Layer Network Design II
B
Dr. Greg Bernstein
Grotto Networking
www.grotto-networking.com

## Slide 2: Outline
Two layer allocation problems
  Link-Path, Single Path Allocation
  Examples
Two layer dimensioning problems
Book Readings
  Section 2.9, Section 12.1 (skip or skim 12.1.5)

## Slide 3: Two layer capacity allocation Problem
Example Ethernet over WDM
  Ethernet demands: {('E1', 'E4'): 23, ('E2', 'E3'): 18, ('E2', 'E6'): 19, ('E3', 'E4'): 17}
  WDM link capacities: 40Gbps

## Slide 4: Example Solutions
Upper layer selected paths:
Lower layer selected paths:
Upper layer link capacities:
Splitting over two different lower layer paths
Optimized objective = 33785.36

## Slide 5: Example Solutions II
Two upper layer paths contribute to the load on link (E1, E2)
Demand on (E1, E2) needs to be split over two different paths [W1, W2] and [W1, W9, W2]

## Slide 6: Two Layer SPA Formulation I
Indices
  Demands
  Links
  Candidate paths
Constants
  Volume of demand d
  Link in path indicator
Variables
  Flow allocation
  Link capacity
Upper Layer

## Slide 7: Two Layer SPA Formulation II
Demand Constraints
Link Capacity Constraints
Upper Layer

## Slide 8: Two Layer SPA Formulation III
Indices
  Links (lower)
  Candidate paths (lower)
Constants
  Link Capacity (lower)
  Link in path indicator (lower)
  Link cost (lower)
Variables
  Flow allocation (lower)
  Path Selection indicator (lower, binary)
Lower Layer

## Slide 9: Two Layer CA Formulation IV
Demand Constraints
Link Capacity Constraints
Path Selection Constraints
Objective
  minimize
Lower Layer

## Slide 10: Variable reduction?
Do we need both and ?
  Can’t we just use as follows:
  Second inequality has two variables multiplied by each other and hence is a non-linear constraint, but we need an linear MIP formulation

## Slide 11: Example SPA Solution I
Upper and Lower layer selected paths:
Upper layer link capacities:
Optimized objective = 35696.34 (previous: 33785.36)

## Slide 12: Example SPA Solution II
Upper layer path: [E1, E2, E4]
Lower layer paths implementing upper layer links:
(E1, E2): [W1, W2]
(E2, E4): [W2, W10, W8, W4]

## Slide 13: Example SPA Solution III
Upper layer path: [E2, E5, E3]
Lower layer paths implementing upper layer links:
(E3, E5): [W3, W5]
(E2, E5): [W2, W8, W5]

## Slide 14: Dimensioning Problems
Looking to size links at both upper and lower layers
  Start simple then deal with modular sizing

## Slide 15: Two Layer Dimensioning Formulation I
Indices
  Demands
  Links
  Candidate paths
Constants
  Volume of demand d
  Link in path indicator
  Cost of upper layer links
Variables
  Flow allocation (continuous)
  Link capacity (continous)
Upper Layer
In CA problems we only cared about lower layer costs. Why would we care here? What values might be assigned?

## Slide 16: Two Layer Dimensioning Formulation II
Demand Constraints
Link Capacity Constraints
Upper Layer

## Slide 17: Two Layer Dimensioning Formulation III
Indices
  Links (lower)
  Candidate paths (lower)
Constants
  Link in path indicator (lower)
  Link cost (lower)
Variables
  Flow allocation (continuous)
  Link Capacity (continuous)
Lower Layer

## Slide 18: Two Layer Dimensioning Formulation IV
Demand Constraints
Link Capacity Constraints
Objective (multi-layer)
  minimize
Lower Layer

## Slide 19: Multi-layer Dim Example Ia
Ethernet over WDM
  Initially continuous variables for link capacities

## Slide 20: Multi-layer Dim Example Ib
Demands
  Upper layer only
  Randomly generated

## Slide 21: Multi-layer Dim Example Ic
Candidate path generation (k-shortest paths alg)
  Upper layer link costs = 1 (why would this be reasonable?)
  Lower layer link costs based on distance
Example best and worst paths
Upper Layer
Lower Layer

## Slide 22: Multi-layer Dim Example Id
Link Size Solutions
Upper Layer
Lower Layer
Dimensioning problem objective = 55,526.56

## Slide 23: Multi-layer Dim Example Ie
Solution Paths
Upper Layer
Lower Layer

## Slide 24: Multi-layer Dim Example If
Upper Layer
Lower Layer
Solution Paths
  Realizing demand (E1, E6): 18.2

## Slide 25: Multi-Layer Dimensioning Modular
But links don’t come in continuous sizes!
  Let M be the size of the capacity for the upper layer links
  Let N be the size of the capacity for the lower layer links
  Use a mix of continuous and integer variables in the formulation

## Slide 26: Two Layer Dimensioning Formulation I
Indices
  Demands
  Links
  Candidate paths
Constants
  Volume of demand d
  Link in path indicator
  Cost of upper layer links
  Upper layer module size M
Variables
  Flow allocation (continuous)
  Link capacity (integer)
Upper Layer

## Slide 27: Two Layer Dimensioning Formulation II
Demand Constraints
Link Capacity Constraints
Upper Layer
Module size times the integer link capacity

## Slide 28: Two Layer Dimensioning Formulation III
Indices
  Links (lower)
  Candidate paths (lower)
Constants
  Link in path indicator (lower)
  Link cost (lower)
  Link Modular Capacity N
Variables
  Flow allocation (integer)
  Link Capacity (integer)
Lower Layer

## Slide 29: Two Layer Dimensioning Formulation IV
Demand Constraints
Link Capacity Constraints
Objective (multi-layer)
  minimize
Lower Layer
Slightly different cost function than text so we can compare to previous results.

## Slide 30: Modular Dimensioning Example 2a
Technology Stack
  10Gbps Ethernet over WDM
  Each wavelength supports 40Gbps of traffic
    Could use G.709 OTU3, OTU3e2
    Or SONET OC-768/ SDH STM-256
In formulation
  M=10
  N=40

## Slide 31: Multi-layer Mod Dim Example 2b
Link Size Solutions
Upper Layer
Lower Layer
Dimensioning problem objective = 71,930.81
Do these link sizes seem correct? Why or Why not?

## Slide 32: Multi-layer Mod Dim Example 2b
Scaled Link Size Solutions
  Need to multiply by modular factors M and N
Upper Layer
Lower Layer

## Slide 33: Multi-layer Mod Dim Example 2c
Upper Layer Solution Paths
Path Splitting!

## Slide 34: Multi-layer Mod Dim Example 2d
Lower Layer Solution Paths
Path Splitting!

## Slide 35: Multi-layer Mod Dim Example 2e
Demand (E2, E6) realization
  Via multiple upper and lower layer paths
Assuming aggregate flows between nodes and Ethernet LAG technology is it okay to split:
Upper layer paths?
Lower layer paths?